## Slide 1
NEW AVIATION CONTROLS ENGINEER ONBOARDING
Simulink in the Aerospace Controls Lifecycle
First-session workflow • model hierarchy • desktop MIL evidence • assurance context
REQUIRE
MODEL
VERIFY
EVIDENCE
FLIGHT-CONTROL SOFTWARE IS AN UNBROKEN CHAIN
AVIATION CONTROLS ENGINEERING ONBOARDING
01
Notes: Timing: 1 minute
Frame this as first-time-user onboarding for aviation controls engineers: operate the saved Simulink models, understand their roles, inspect results, and trace one classroom requirement to retained evidence. The examples are executable and reviewable, but deliberately small and non-production.
Caveats
- Illustrative classroom requirements — not production aircraft data or an approved certification baseline.
- The package demonstrates desktop model work; it is not a completed certification package.
[Sources]
- README.md
- results/validation_summary.txt

## Slide 2
ORIENTATION
The executable model is the engineering hub
AVIATION CONTROLS ENGINEERING ONBOARDING
02
EXECUTABLE
MODEL
Requirements
Control design
Simulation
Verification
The same behavior can be discussed, simulated, reviewed, tested, integrated, and traced.
MODEL-BASED DESIGN
Notes: Timing: 2 minutes
Use this hub to establish the model roles before opening files. AircraftFeedbackControlLoop is the standalone closed-loop learning model; ReferencedFlightControlArchitecture is the integration parent; four models are referenced children; AutopilotModeLogic is a separate Stateflow example; and PitchRateLimiter_Harness is the independent component-test harness.
Caveats
- A top-level model is selected for the engineering task; there is no single model that serves every role.
- AutopilotModeLogic is not a child of the referenced integration architecture.
[Sources]
- README.md
- models/AircraftFeedbackControlLoop.slx
- models/ReferencedFlightControlArchitecture.slx

## Slide 3
ORIENTATION
Your first session: orient, execute, inspect, trace
AVIATION CONTROLS ENGINEERING ONBOARDING
03
Operate a model — initialize paths; open, update, run, stop, and inspect results
Navigate the editor — Simulation, Debug, Modeling, and Apps
Read semantics — units, data types, dimensions, timing, and logging
Trace behavior — top level → component → harness → executed evidence
1 START + RUN
2 MODEL HIERARCHY
3 OVERLAYS
4 DATA INSPECTOR
5 TRACEABILITY
Keep asking: Which model am I in, what state is visible, and what evidence proves the requirement?
Notes: Timing: 1 minute
Preview the learning sequence: initialize and operate a model, navigate the editor, read hierarchy and overlays, inspect logged data, then follow requirement intent into implementation and evidence. Ask throughout: which model am I in, what is visible, and what objective result supports the claim?
Caveats
- The sequence is a learning path, not a substitute for approved project procedures.
[Sources]
- README.md

## Slide 4
01 • FIRST SESSION
MATLAB computes; Simulink exposes behavior
AVIATION CONTROLS ENGINEERING ONBOARDING
04
MATLAB
SIMULINK
Best at — scripts, algorithms, matrices, optimization, data analysis
Execution — statements and functions run in defined order
View — variables, arrays, figures, tables, reports
Best at — dynamic systems, feedback, hybrid logic, integration
Execution — blocks exchange signals over simulated time
View — data flow, hierarchy, state, sample time, interfaces
They are one environment: MATLAB configures, analyzes, automates, and reports on Simulink models.
Notes: Timing: 2 minutes
MATLAB and Simulink are complementary. MATLAB prepares controlled data, automates operations, evaluates results, and writes evidence; Simulink exposes executable time behavior, hierarchy, state, interfaces, and sample times. In this repository, MATLAB scripts drive and assess the saved Simulink models.
Caveats
- The distinction is about representation and workflow, not competing tools.
- A script that runs a model is not itself proof that every lifecycle objective is satisfied.
[Sources]
- scripts/run_training_simulations.m
- scripts/run_pitch_rate_limiter_tests.m
- https://www.mathworks.com/help/simulink/gs/model-based-design.html

## Slide 5
01 • FIRST SESSION
Start in the repository, then distinguish every action
AVIATION CONTROLS ENGINEERING ONBOARDING
05
01
INITIALIZE
Command Window
Prepare paths + FCS_Data.sldd
02
OPEN
Ctrl+O / open_system
Choose the correct top level
03
UPDATE
Modeling • Ctrl+D
Compile and propagate semantics
04
RUN
Simulation • Ctrl+T
Execute desktop model behavior
05
STOP
Simulation • Stop
Interrupt the current execution
06
BUILD
Apps • Ctrl+B
Configured code generation only
07
TEST
MATLAB driver
Run harness assessments
FIRST CLOSED-LOOP SESSION — MATLAB EQUIVALENTS
projectRoot = 'D:\GitHub\aviation-controls-simulink-training';
addpath(fullfile(projectRoot,'scripts'), fullfile(projectRoot,'models'), fullfile(projectRoot,'data'));
initialize_training_data(projectRoot);
open_system(fullfile(projectRoot,'models','AircraftFeedbackControlLoop.slx'));
set_param('AircraftFeedbackControlLoop','SimulationCommand','update');
sim('AircraftFeedbackControlLoop');
run_pitch_rate_limiter_tests(projectRoot);
SUCCESS LOOKS LIKE
• Training data dictionary ready
• Update completes without an error
• Simulation outputs appear under results/
• Limiter driver writes CSV + MAT
• Human-readable HTML + PNG appear under reports/
Build remains optional and scope-dependent; no production-code claim is made.
Notes: Timing: 3 minutes
Start MATLAB R2023b in the repository, add the scripts, models, and data folders to the path, run initialize_training_data(projectRoot), and open models/AircraftFeedbackControlLoop.slx for the first closed-loop exercise. Update the diagram, run, stop if needed, and inspect outputs under results; use the helper scripts for repeatable simulations and evidence refresh.
Caveats
- There is no MATLAB Project .prj file in this repository; say initialize the training package, not open a project file.
- Use refresh_onboarding_artifacts after layout-safe changes; regenerate_all recreates models and can overwrite manually cleaned layouts.
[Sources]
- README.md
- scripts/initialize_training_data.m
- scripts/refresh_onboarding_artifacts.m
- https://www.mathworks.com/help/simulink/slref/simulinkeditor.html

## Slide 6
The toolstrip tells you where each action lives
06
01 • FIRST SESSION
AVIATION CONTROLS ENGINEERING ONBOARDING
SIMULATION
Open • Run • Stop • Data Inspector
DEBUG
Diagnostics • Information Overlays
MODELING
Update Model • configuration
FORMAT
Layout • labels • visual review
APPS
Testing tools • code generation
Select the tab, then the action. Open, update, run, stop, build, and test create different engineering states and evidence.
Notes: Timing: 3 minutes
Orient learners to the Simulation, Debug, Modeling, Format, and Apps tabs. Open chooses the artifact; Update Diagram or Ctrl+D compiles and propagates model semantics; Run executes a simulation; Stop interrupts it; Build or Ctrl+B is a separate configured code-generation action; and test execution invokes the harness driver and assessments.
Caveats
- Update/compile is not simulation, and Run is not Build.
- The package makes no production-code, generated-code verification, SIL, PIL, or HIL claim; Embedded Coder is unavailable.
[Sources]
- results/environment_inventory.txt
- https://www.mathworks.com/help/simulink/slref/simulinkeditor.html
- https://www.mathworks.com/help/simulink/ug/summary-of-mouse-and-keyboard-actions.html
- https://www.mathworks.com/help/rtw/ug/generating-code-using-simulink-coder.html

## Slide 7
01 • FIRST SESSION
Turn model displays on—and off—for focus
AVIATION CONTROLS ENGINEERING ONBOARDING
07
DEBUG → INFORMATION OVERLAYS
PORT UNITS
ShowPortUnits
DATA TYPES
ShowPortDataTypes
DIMENSIONS
ShowLineDimensions
SIGNAL NAMES
line labels + propagated names
LOGGING BADGES
DataLogging + model SignalLogging
TEST POINTS
ShowTestPointIcons, when supported
MODEL OVERLAYS — units, types, dimensions, names, and log/test-point badges annotate the diagram.
SDI MARKERS — cursors and data points annotate logged traces. Neither display changes behavior.
Notes: Timing: 3 minutes
Use Debug > Information Overlays to reveal port units, data types, signal dimensions, names, and logging or test-point badges; turn each display off again when it obscures structure. These overlays describe model semantics and instrumentation. Simulation Data Inspector markers and cursors instead annotate plotted samples after data has been logged.
Caveats
- A marker does not create or delete a logged data point.
- Some overlays require a successful model update before propagated attributes are available, and exact toolstrip grouping can vary by release or selection.
[Sources]
- https://www.mathworks.com/help/simulink/ug/displaying-units.html
- https://www.mathworks.com/help/simulink/ug/working-with-test-points.html
- https://www.mathworks.com/help/simulink/ug/view-the-signal-logging-configuration.html
- https://www.mathworks.com/help/simulink/gui/signallogging.html

## Slide 8
03 • SIMULATION DATA INSPECTOR
Data Inspector reveals one saved run
AVIATION CONTROLS ENGINEERING ONBOARDING
24
ONE RUN
AircraftFeedbackControlLoop — onboarding reference
FIVE SIGNALS
command • response • error • actuator • disturbance
THREE PLOTS
tracking • error • actuator + disturbance
WHY USE SDI
inspect without model edits • compare • zoom • cursors • units • export
Markers show logged samples; model overlays show model metadata. Opening a saved session can replace the current SDI repository.
Notes: Timing: 4 minutes
The saved onboarding Data Inspector setup contains one run and five signals arranged in three vertical plots: command versus response, tracking error, and actuator versus disturbance. Use legends, units, zoom, cursors, and markers to inspect timing and transients, compare future executions, and retain reviewable evidence without modifying the model.
Caveats
- Desktop Simulink model execution (MIL); not SIL, PIL, or HIL.
- Opening a saved SDI session can replace the current repository. The provided open helper refuses by default when runs exist; explicit replacement creates recoverable backups.
- The two .mldatx files are SDI view/session artifacts, not Simulink Test files.
[Sources]
- screenshots/SimulationDataInspector_Onboarding.jpg
- data/SimulationDataInspector/AircraftFeedbackControlLoop_Onboarding_View.mldatx
- results/SimulationDataInspector/AircraftFeedbackControlLoop_Onboarding_Session.mldatx
- scripts/open_data_inspector_reference.m
- scripts/update_data_inspector.m
- scripts/save_data_inspector_reference.m
- https://www.mathworks.com/help/simulink/slref/simulationdatainspector.html
- https://www.mathworks.com/help/simulink/ug/compare-simulation-data.html
- https://www.mathworks.com/help/simulink/slref/simulink.sdi.setmarkerson.html

## Slide 9
03 • SIMULATION DATA INSPECTOR
Data Inspector reveals one saved run
AVIATION CONTROLS ENGINEERING ONBOARDING
24
ONE RUN
AircraftFeedbackControlLoop — onboarding reference
FIVE SIGNALS
command • response • error • actuator • disturbance
THREE PLOTS
tracking • error • actuator + disturbance
WHY USE SDI
inspect without model edits • compare • zoom • cursors • units • export
Markers show logged samples; model overlays show model metadata. Opening a saved session can replace the current SDI repository.
Notes: Timing: 4 minutes
The saved onboarding Data Inspector setup contains one run and five signals arranged in three vertical plots: command versus response, tracking error, and actuator versus disturbance. Use legends, units, zoom, cursors, and markers to inspect timing and transients, compare future executions, and retain reviewable evidence without modifying the model.
Caveats
- Desktop Simulink model execution (MIL); not SIL, PIL, or HIL.
- Opening a saved SDI session can replace the current repository. The provided open helper refuses by default when runs exist; explicit replacement creates recoverable backups.
- The two .mldatx files are SDI view/session artifacts, not Simulink Test files.
[Sources]
- screenshots/SimulationDataInspector_Onboarding.jpg
- data/SimulationDataInspector/AircraftFeedbackControlLoop_Onboarding_View.mldatx
- results/SimulationDataInspector/AircraftFeedbackControlLoop_Onboarding_Session.mldatx
- scripts/open_data_inspector_reference.m
- scripts/update_data_inspector.m
- scripts/save_data_inspector_reference.m
- https://www.mathworks.com/help/simulink/slref/simulationdatainspector.html
- https://www.mathworks.com/help/simulink/ug/compare-simulation-data.html
- https://www.mathworks.com/help/simulink/slref/simulink.sdi.setmarkerson.html

## Slide 10
07 • AUTOMATION & ENVIRONMENTS
CI automates evidence production—not approval
AVIATION CONTROLS ENGINEERING ONBOARDING
37
Commit
Jenkinsfile
Build / Update
Model Checks
Tests
Reports + Artifacts
GROOVY / JENKINSFILE
orchestrates stages, agents, parameters, parallel branches, retention
MATLAB + SIMULINK
initializes the repository, updates models, runs checks and the MATLAB harness driver; the two retained .mldatx files are SDI artifacts—not Test Manager suites
ROBOT FRAMEWORK
optional keyword-driven orchestration for benches, external interfaces, and system tests
A green pipeline is controlled evidence input—not certification approval.
Notes: Timing: 3 minutes
Treat CI as an orchestrator around controlled engineering commands: initialize, update models, run simulations and assessments, validate outputs, and retain reports. A green stage says the configured steps passed on that agent and baseline; reviewers still examine warnings, scope, traceability, failures, and configuration.
Caveats
- No Jenkins pipeline was executed for this package.
- A passing pipeline is evidence input, not certification approval.
[Sources]
- results/validation_summary.txt
- scripts/validate_training_project.m
- https://www.mathworks.com/help/sltest/ug/output-results-for-continuous-integration-systems.html
- https://www.faa.gov/documentLibrary/media/Order/FAA_Order_8110.49A.pdf

## Slide 11
01 • FIRST SESSION
MATLAB computes; Simulink exposes behavior
AVIATION CONTROLS ENGINEERING ONBOARDING
04
MATLAB
SIMULINK
Best at — scripts, algorithms, matrices, optimization, data analysis
Execution — statements and functions run in defined order
View — variables, arrays, figures, tables, reports
Best at — dynamic systems, feedback, hybrid logic, integration
Execution — blocks exchange signals over simulated time
View — data flow, hierarchy, state, sample time, interfaces
They are one environment: MATLAB configures, analyzes, automates, and reports on Simulink models.
Notes: Timing: 2 minutes
MATLAB and Simulink are complementary. MATLAB prepares controlled data, automates operations, evaluates results, and writes evidence; Simulink exposes executable time behavior, hierarchy, state, interfaces, and sample times. In this repository, MATLAB scripts drive and assess the saved Simulink models.
Caveats
- The distinction is about representation and workflow, not competing tools.
- A script that runs a model is not itself proof that every lifecycle objective is satisfied.
[Sources]
- scripts/run_training_simulations.m
- scripts/run_pitch_rate_limiter_tests.m
- https://www.mathworks.com/help/simulink/gs/model-based-design.html

## Slide 12
02 • MODEL HIERARCHY & GALLERY
The current job determines which model is top level
AVIATION CONTROLS ENGINEERING ONBOARDING
08
STANDALONE CLOSED LOOP
REFERENCED INTEGRATION
SEPARATE TRAINING MODELS
AircraftFeedbackControlLoop.slx
standalone simulation top level
Pitch Controller PI
Actuator Dynamics
Simplified Longitudinal
Aircraft Dynamics
Sensor Processing Lag
ReferencedFlightControl
Architecture.slx • integration parent
SensorProcessingRef.slx
referenced child
PitchRateLimiter.slx
→ Pitch Rate Limiter Logic
PitchControllerRef.slx
→ Pitch Rate PI
ActuatorCommandRef.slx
referenced child
AutopilotModeLogic.slx • separate root
Autopilot Mode Logic
Stateflow chart • internal
PitchRateLimiter_Harness.slx
independent harness
Unit Under Test - PitchRateLimiter
model reference
Root model • referenced child • internal subsystem/chart • independent harness
Notes: Timing: 2 minutes
Read the hierarchy by role. The standalone feedback loop contains four internal subsystems; the Stateflow model contains Autopilot Mode Logic; the referenced architecture owns four child models; PitchRateLimiter and PitchControllerRef each expose one meaningful internal subsystem; and the harness references the same limiter component used by integration.
Caveats
- Use the exact saved path AutopilotModeLogic/Autopilot Mode Logic; Stateflow describes the technology, not the block name.
- Referenced child models, internal subsystems, and an independent harness are different hierarchy relationships.
[Sources]
- README.md
- screenshots/VisualManifest.csv
- https://www.mathworks.com/help/simulink/ug/overview-of-model-referencing-1.html

## Slide 13
02 • MODEL HIERARCHY & GALLERY
AircraftFeedbackControlLoop closes the training loop
AVIATION CONTROLS ENGINEERING ONBOARDING
09
ROOT MODEL
models/AircraftFeedbackControlLoop.slx • standalone closed-loop training model
Notes: Timing: 2 minutes
Trace AircraftFeedbackControlLoop from pitch command through controller, actuator, simplified longitudinal plant, and sensor lag back to the error calculation. The model logs command, response, error, actuator, and disturbance signals for the retained desktop run.
Caveats
- This is a simplified standalone training loop, not production aircraft dynamics.
- Its simulation result is MIL evidence only.
[Sources]
- models/AircraftFeedbackControlLoop.slx
- screenshots/AircraftFeedbackControlLoop_Editor.jpg
- results/AircraftFeedback_CommandTracking.csv

## Slide 14
02 • MODEL HIERARCHY & GALLERY
Pitch Controller PI turns tracking error into demand
AVIATION CONTROLS ENGINEERING ONBOARDING
10
INTERNAL SUBSYSTEM
AircraftFeedbackControlLoop/Pitch Controller PI
Notes: Timing: 2 minutes
Inside AircraftFeedbackControlLoop/Pitch Controller PI, identify proportional and integral paths and the discrete state. The separate subsystem boundary lets reviewers distinguish controller behavior from actuator saturation, plant dynamics, and sensing.
Caveats
- The gains and initial condition come from controlled training data and are not aircraft-program values.
[Sources]
- models/AircraftFeedbackControlLoop.slx
- screenshots/AircraftFeedback_PitchController.png
- data/FCS_Data.sldd

## Slide 15
02 • MODEL HIERARCHY & GALLERY
Actuator Dynamics converts demand into position
AVIATION CONTROLS ENGINEERING ONBOARDING
11
INTERNAL SUBSYSTEM
AircraftFeedbackControlLoop/Actuator Dynamics
Notes: Timing: 2 minutes
AircraftFeedbackControlLoop/Actuator Dynamics turns controller demand into a bounded, lagged actuator response. Point out where amplitude limiting and discrete dynamics enter, then connect those choices to explicit units, parameters, and initial state.
Caveats
- This actuator is an illustrative dynamic element, not a qualified actuator model or hardware measurement.
[Sources]
- models/AircraftFeedbackControlLoop.slx
- screenshots/AircraftFeedback_ActuatorDynamics.png
- data/FCS_Data.sldd

## Slide 16
02 • MODEL HIERARCHY & GALLERY
Longitudinal dynamics turn actuator motion into response
AVIATION CONTROLS ENGINEERING ONBOARDING
12
INTERNAL SUBSYSTEM
AircraftFeedbackControlLoop/Simplified Longitudinal Aircraft Dynamics
Notes: Timing: 2 minutes
AircraftFeedbackControlLoop/Simplified Longitudinal Aircraft Dynamics converts actuator command and disturbance into pitch-rate and pitch-angle response. Use the view to discuss state, feedback, and disturbance entry without treating the coefficients as validated aerodynamics.
Caveats
- The plant is intentionally simplified and unsuitable for aircraft-performance claims.
[Sources]
- models/AircraftFeedbackControlLoop.slx
- screenshots/AircraftFeedback_LongitudinalPlant.png
- data/FCS_Data.sldd

## Slide 17
02 • MODEL HIERARCHY & GALLERY
Sensor Processing Lag exposes measurement dynamics
AVIATION CONTROLS ENGINEERING ONBOARDING
13
INTERNAL SUBSYSTEM
AircraftFeedbackControlLoop/Sensor Processing Lag
Notes: Timing: 2 minutes
AircraftFeedbackControlLoop/Sensor Processing Lag closes the loop with a discrete filtered measurement. Ask learners to identify the filter state, controlled coefficient, initial condition, output unit, and relationship between model rate and apparent response delay.
Caveats
- A desktop sensor-lag model is not sensor qualification or bench evidence.
[Sources]
- models/AircraftFeedbackControlLoop.slx
- screenshots/AircraftFeedback_SensorProcessingLag.png
- data/FCS_Data.sldd

## Slide 18
02 • MODEL HIERARCHY & GALLERY
AutopilotModeLogic wraps mode behavior in explicit interfaces
AVIATION CONTROLS ENGINEERING ONBOARDING
14
ROOT MODEL
models/AutopilotModeLogic.slx • separate Stateflow training model
Notes: Timing: 2 minutes
At the AutopilotModeLogic root, identify external mode requests, validity and fault inputs, the Stateflow subsystem, and the documented mode output. The root view is the interface contract; the transition behavior is one level down.
Caveats
- The mode codes and transitions are illustrative classroom behavior, not an approved autopilot specification.
[Sources]
- models/AutopilotModeLogic.slx
- screenshots/AutopilotModeLogic_Model.png
- data/FCSMode.m

## Slide 19
02 • MODEL HIERARCHY & GALLERY
Stateflow guards OFF, ARMED, ENGAGED, and DEGRADED
AVIATION CONTROLS ENGINEERING ONBOARDING
15
INTERNAL STATEFLOW VIEW
AutopilotModeLogic/Autopilot Mode Logic • Stateflow chart
Notes: Timing: 2 minutes
Open AutopilotModeLogic/Autopilot Mode Logic and read OFF, ARMED, ENGAGED, and DEGRADED as executable state logic. Follow guards and reset paths, then relate them to the retained mode-sequence result rather than relying only on visual inspection.
Caveats
- The exact current block and chart name is Autopilot Mode Logic; do not prefix the saved path with Stateflow.
- A visited-state plot is evidence for this scenario, not exhaustive state or transition coverage.
[Sources]
- models/AutopilotModeLogic.slx
- screenshots/AutopilotModeLogic_Stateflow_Editor.jpg
- results/AutopilotModeSequence.csv
- https://www.mathworks.com/help/stateflow/state-transition-charts.html

## Slide 20
02 • MODEL HIERARCHY & GALLERY
ReferencedFlightControlArchitecture is the integration top level
AVIATION CONTROLS ENGINEERING ONBOARDING
16
INTEGRATION PARENT
models/ReferencedFlightControlArchitecture.slx • model-reference integration parent
Notes: Timing: 3 minutes
ReferencedFlightControlArchitecture is the integration parent. It creates FlightControlBus, invokes Sensor Processing, Pitch Rate Limiter, Pitch Controller, and Actuator Command Model blocks, and exposes integrated outputs. Model-reference boundaries make ownership and interface compatibility reviewable.
Caveats
- The architecture update proves resolvable interfaces and configuration, not compliance with behavioral requirements.
- On the verified student license, Accelerator Model blocks fall back to Normal mode.
[Sources]
- models/ReferencedFlightControlArchitecture.slx
- screenshots/ReferencedFlightControlArchitecture_Editor.jpg
- results/ReferencedArchitecture_Validation.csv
- https://www.mathworks.com/help/simulink/ug/overview-of-model-referencing-1.html

## Slide 21
02 • MODEL HIERARCHY & GALLERY
SensorProcessingRef owns the referenced sensor contract
AVIATION CONTROLS ENGINEERING ONBOARDING
17
REFERENCED CHILD
models/SensorProcessingRef.slx
Notes: Timing: 2 minutes
SensorProcessingRef is the referenced sensor-processing child. Review its FlightControlBus input and output, validity handling, filtering, and explicit interface rather than reading it as an isolated top-level simulation.
Caveats
- Its primary role here is a referenced integration component, not the standalone closed-loop entry point.
[Sources]
- models/SensorProcessingRef.slx
- screenshots/SensorProcessingRef_Model.png
- results/FlightControlBus_Inventory.csv

## Slide 22
02 • MODEL HIERARCHY & GALLERY
PitchRateLimiter is a separately managed component
AVIATION CONTROLS ENGINEERING ONBOARDING
18
REFERENCED CHILD / COMPONENT
models/PitchRateLimiter.slx • standalone component and referenced child
Notes: Timing: 2 minutes
PitchRateLimiter is both a reviewable component model and a referenced child. Its root exposes q_cmd_in, normal_mode, input_valid, q_cmd_out, and limiter_active at the controlled 50 Hz sample time, while implementation detail remains inside Pitch Rate Limiter Logic.
Caveats
- This is a magnitude limiter, not a slew-rate limiter.
- The values and requirements are illustrative training data.
[Sources]
- models/PitchRateLimiter.slx
- screenshots/PitchRateLimiter_Model.png
- docs/PitchRateLimiter_Requirements_Traceability.csv

## Slide 23
02 • MODEL HIERARCHY & GALLERY
Pitch Rate Limiter Logic clamps magnitude and controls fallback
AVIATION CONTROLS ENGINEERING ONBOARDING
19
INTERNAL SUBSYSTEM
PitchRateLimiter/Pitch Rate Limiter Logic
Notes: Timing: 3 minutes
Inside PitchRateLimiter/Pitch Rate Limiter Logic, Magnitude Clamp applies the inclusive ±q_limit_normal bound; Normal AND Valid controls Select Valid Command; Training Fallback Command supplies zero; and the comparison and logic blocks form limiter_active. Use the exact block names because they anchor traceability.
Caveats
- Exactly ±12 deg/s is not clamped active; strictly outside the limits is active only during valid Normal operation.
- Do not describe Magnitude Clamp as rate-of-change limiting.
[Sources]
- models/PitchRateLimiter.slx
- screenshots/PitchRateLimiter_Implementation.png
- docs/PitchRateLimiter_Requirements_Traceability.csv

## Slide 24
02 • MODEL HIERARCHY & GALLERY
PitchControllerRef defines the referenced controller boundary
AVIATION CONTROLS ENGINEERING ONBOARDING
20
REFERENCED CHILD
models/PitchControllerRef.slx
Notes: Timing: 2 minutes
PitchControllerRef is the referenced controller child used by the integration parent. Its root contract accepts limited command and feedback and produces actuator demand and tracking error, separating interface review from the internal PI implementation.
Caveats
- Do not confuse this referenced child with AircraftFeedbackControlLoop/Pitch Controller PI; they are distinct saved artifacts.
[Sources]
- models/PitchControllerRef.slx
- screenshots/PitchControllerRef_Model.png

## Slide 25
02 • MODEL HIERARCHY & GALLERY
Pitch Rate PI implements the referenced control law
AVIATION CONTROLS ENGINEERING ONBOARDING
21
INTERNAL SUBSYSTEM
PitchControllerRef/Pitch Rate PI
Notes: Timing: 2 minutes
PitchControllerRef/Pitch Rate PI exposes the referenced controller's proportional and integral behavior. Review its error formation, gains, integrator state, and output contract, then return to the parent model to see how the component is connected.
Caveats
- The exact internal path is PitchControllerRef/Pitch Rate PI.
[Sources]
- models/PitchControllerRef.slx
- screenshots/PitchControllerRef_PitchRatePI.png
- data/FCS_Data.sldd

## Slide 26
02 • MODEL HIERARCHY & GALLERY
ActuatorCommandRef owns command limiting and status
AVIATION CONTROLS ENGINEERING ONBOARDING
22
REFERENCED CHILD
models/ActuatorCommandRef.slx
Notes: Timing: 2 minutes
ActuatorCommandRef is the referenced actuator-command child. It receives actuator demand and returns the bounded command plus an active-status output, making command limiting and status propagation explicit at the integration boundary.
Caveats
- This component demonstrates interface and command-processing patterns; it is not actual actuator hardware or HIL evidence.
[Sources]
- models/ActuatorCommandRef.slx
- screenshots/ActuatorCommandRef_Model.png

## Slide 27
02 • MODEL HIERARCHY & GALLERY
PitchRateLimiter_Harness isolates the unit under test
AVIATION CONTROLS ENGINEERING ONBOARDING
23
INDEPENDENT TEST HARNESS
models/PitchRateLimiter_Harness.slx • references PitchRateLimiter
Notes: Timing: 3 minutes
PitchRateLimiter_Harness is an independent executable Simulink model. From Workspace blocks provide the three deterministic inputs; the exact Model block PitchRateLimiter_Harness/Unit Under Test - PitchRateLimiter references the component; and To Workspace blocks retain q_cmd_out and limiter_active for external MATLAB assessments.
Caveats
- This is a standalone Simulink harness, not a Simulink Test harness or Test Manager suite.
- Expected values, tolerances, and pass/fail logic live in run_pitch_rate_limiter_tests.m, not inside the harness.
[Sources]
- models/PitchRateLimiter_Harness.slx
- screenshots/PitchRateLimiter_Harness.png
- scripts/run_pitch_rate_limiter_tests.m

## Slide 28
04 • ASSURANCE CONTEXT
DO-178C defines objectives; DO-331 addresses model use
AVIATION CONTROLS ENGINEERING ONBOARDING
25
DO-178C
Defines — objectives, activities, and life-cycle data
Scales — rigor according to software level
Covers — planning, development, verification, CM, QA, liaison
DO-331
Supplements — DO-178C for model-based development and verification
Clarifies — model roles, model standards, verification, and traceability
Does not — make models or generated code automatically compliant
The project plans define whether a model is specification, design, source, or verification material—and which objectives apply.
Notes: Timing: 3 minutes
FAA AC 20-115D recognizes DO-178C as an accepted means of compliance with applicable airworthiness regulations and recognizes DO-331 as its model-based development and verification supplement. Project plans determine how a model is used and which objectives and lifecycle data apply.
Caveats
- DO-178C is not a standalone software certificate.
- DO-331 supplements DO-178C; a Simulink model is not automatically compliant.
[Sources]
- https://www.faa.gov/regulations_policies/advisory_circulars/index.cfm/go/document.information/documentID/1032046
- https://www.faa.gov/documentLibrary/media/Order/FAA_Order_8110.49A.pdf

## Slide 29
03 • SIMULATION DATA INSPECTOR
Data Inspector reveals one saved run
AVIATION CONTROLS ENGINEERING ONBOARDING
24
ONE RUN
AircraftFeedbackControlLoop — onboarding reference
FIVE SIGNALS
command • response • error • actuator • disturbance
THREE PLOTS
tracking • error • actuator + disturbance
WHY USE SDI
inspect without model edits • compare • zoom • cursors • units • export
Markers show logged samples; model overlays show model metadata. Opening a saved session can replace the current SDI repository.
Notes: Timing: 4 minutes
The saved onboarding Data Inspector setup contains one run and five signals arranged in three vertical plots: command versus response, tracking error, and actuator versus disturbance. Use legends, units, zoom, cursors, and markers to inspect timing and transients, compare future executions, and retain reviewable evidence without modifying the model.
Caveats
- Desktop Simulink model execution (MIL); not SIL, PIL, or HIL.
- Opening a saved SDI session can replace the current repository. The provided open helper refuses by default when runs exist; explicit replacement creates recoverable backups.
- The two .mldatx files are SDI view/session artifacts, not Simulink Test files.
[Sources]
- screenshots/SimulationDataInspector_Onboarding.jpg
- data/SimulationDataInspector/AircraftFeedbackControlLoop_Onboarding_View.mldatx
- results/SimulationDataInspector/AircraftFeedbackControlLoop_Onboarding_Session.mldatx
- scripts/open_data_inspector_reference.m
- scripts/update_data_inspector.m
- scripts/save_data_inspector_reference.m
- https://www.mathworks.com/help/simulink/slref/simulationdatainspector.html
- https://www.mathworks.com/help/simulink/ug/compare-simulation-data.html
- https://www.mathworks.com/help/simulink/slref/simulink.sdi.setmarkerson.html

## Slide 30
04 • ASSURANCE CONTEXT
DO-178C defines objectives; DO-331 addresses model use
AVIATION CONTROLS ENGINEERING ONBOARDING
25
DO-178C
Defines — objectives, activities, and life-cycle data
Scales — rigor according to software level
Covers — planning, development, verification, CM, QA, liaison
DO-331
Supplements — DO-178C for model-based development and verification
Clarifies — model roles, model standards, verification, and traceability
Does not — make models or generated code automatically compliant
The project plans define whether a model is specification, design, source, or verification material—and which objectives apply.
Notes: Timing: 3 minutes
FAA AC 20-115D recognizes DO-178C as an accepted means of compliance with applicable airworthiness regulations and recognizes DO-331 as its model-based development and verification supplement. Project plans determine how a model is used and which objectives and lifecycle data apply.
Caveats
- DO-178C is not a standalone software certificate.
- DO-331 supplements DO-178C; a Simulink model is not automatically compliant.
[Sources]
- https://www.faa.gov/regulations_policies/advisory_circulars/index.cfm/go/document.information/documentID/1032046
- https://www.faa.gov/documentLibrary/media/Order/FAA_Order_8110.49A.pdf

## Slide 31
04 • ASSURANCE CONTEXT
Software levels scale rigor—and independence is planned
AVIATION CONTROLS ENGINEERING ONBOARDING
26
DO-178C SOFTWARE LEVEL
INDEPENDENCE IS OBJECTIVE-SPECIFIC
A
Catastrophic
highest applicable rigor + independence
B
Hazardous / Severe-Major
very high rigor
C
Major
substantial verification rigor
D
Minor
reduced objective set
E
No Effect
no DO-178C objectives apply
PLANNED
Approved plans designate which verification objectives require independence.
ROLE-BASED
Where required, the author is not the sole independent verifier of their own work.
EVIDENCED
Review records identify the verifier, activity, baseline, findings, and disposition.
Use “DO-178C Software Level A” unless discussing a broader system DAL allocation.
Notes: Timing: 3 minutes
Software level originates in the system safety process and drives the applicable objective and independence framework. Say DO-178C Software Level A when discussing software; reserve DAL terminology for the broader system allocation context. Independence is planned for designated verification objectives and must be demonstrated through roles and evidence.
Caveats
- An author should not be the sole independent verifier of their own work where independence is required.
- A summary slide cannot replace the approved plans, certification basis, or objective tables.
[Sources]
- https://www.faa.gov/regulations_policies/advisory_circulars/index.cfm/go/document.information/documentID/1032046
- https://www.faa.gov/documentLibrary/media/Order/FAA_Order_8110.49A.pdf

## Slide 32
Traceability turns artifacts into evidence
27
Requirement
Model element
Test case
Verification result
BIDIRECTIONAL: every artifact has a reason to exist; every requirement has objective coverage
EVIDENCE PACKAGE
plans + standards
review records
test procedures + results
coverage + analyses
configuration + problem reports
Pipeline and test results are evidence inputs—not automatic approval.
04 • ASSURANCE CONTEXT
AVIATION CONTROLS ENGINEERING ONBOARDING
Notes: Timing: 3 minutes
Traceability is bidirectional: requirement to implementing artifact and objective verification, then result and model element back to justified intent. This package demonstrates that chain through a traceability CSV, an executable script, retained CSV/MAT results, and a human-readable report.
Caveats
- The package has no live Simulink Requirements links because Simulink Requirements is unavailable.
- A passing pipeline or test result is evidence input, not certification approval.
[Sources]
- docs/PitchRateLimiter_Requirements_Traceability.csv
- results/environment_inventory.txt
- https://www.faa.gov/documentLibrary/media/Order/FAA_Order_8110.49A.pdf
- https://www.mathworks.com/help/slrequirements/ug/create-and-store-links.html

## Slide 33
04 • ASSURANCE CONTEXT
The V-model pairs every definition with verification
AVIATION CONTROLS ENGINEERING ONBOARDING
28
REQUIREMENTS ↔ BIDIRECTIONAL TRACEABILITY
MODEL-BASED · MATLAB / SIMULINK
INDEPENDENT VERIFICATION ACTIVITIES
INTEGRATION + EXECUTION ENVIRONMENTS
DEFINE + DECOMPOSE · REVIEW GATES G1–G5
PAIR EACH LEVEL
INTEGRATE + VERIFY + VALIDATE
System / engine
requirements
System verification
+ validation
Software high-level
requirements (HLR)
Software integration
verification
Software architecture / design
+ low-level requirements
Component / unit
verification
Simulink models
+ C/H source code
MIL / SIL · analysis
+ coverage
Executable
object code
PIL / target · HIL / bench
+ system integration
G1
G2
G3
G4
G5
CONTROLLED SOFTWARE BASELINE
configuration · trace links · review records
Agile changes the cadence; it does not remove ordered reviews, traceability, controlled baselines, or planned independence.
Notes: Timing: 3 minutes
Use the V-model as a relationship map between definition, realization, and verification rather than as a mandate for one schedule. Agile and waterfall can both organize compliant work, but cadence never removes lifecycle data, traceability, reviews, configuration control, baselines, problem reporting, or required independence.
Caveats
- Process labels do not establish compliance; approved plans and objective evidence do.
[Sources]
- https://www.nasa.gov/reference/systems-engineering-handbook/
- https://www.faa.gov/documentLibrary/media/Order/FAA_Order_8110.49A.pdf

## Slide 34
05 • REQUIREMENTS & TRACEABILITY
Illustrative requirements make the training chain explicit
SYSTEM
PSYS-001
Before the pitch controller, constrain a valid Normal-mode pitch-rate command to |q_cmd| ≤ 12 deg/s; otherwise substitute 0 deg/s.
SOFTWARE HLR SWHLR-001 / PRL-001
When normal_mode and input_valid are true, q_cmd_out = min(max(q_cmd_in, −12), +12); otherwise q_cmd_out = 0 deg/s.
SOFTWARE LLR / DESIGN SWLLR-001
Magnitude Clamp applies ±q_limit_normal; Normal AND Valid drives Select Valid Command; Training Fallback Command is 0 deg/s.
STATUS + TIMING PRL-003 / PRL-004
limiter_active is true only outside ±12 during valid Normal mode; the component updates at 50 Hz with no added state dynamics.
Illustrative classroom requirements — not production aircraft data or an approved certification baseline.
AVIATION CONTROLS ENGINEERING ONBOARDING
29
Notes: Timing: 3 minutes
Walk from the classroom system intent through a software HLR and an implementation-oriented LLR or design statement. Connect the inclusive ±12 deg/s behavior, zero fallback, limiter status, and 50 Hz execution to PRL-001 through PRL-005 and the exact saved blocks.
Caveats
- Illustrative classroom requirements — not production aircraft data or an approved certification baseline.
- PSYS-001, SWHLR-001, and SWLLR-001 are presentation-level classroom mappings; the repository traceability CSV contains PRL-001 through PRL-005.
[Sources]
- docs/PitchRateLimiter_Requirements_Traceability.csv
- models/PitchRateLimiter.slx
- https://www.faa.gov/regulations_policies/advisory_circulars/index.cfm/go/document.information/documentID/1032046

## Slide 35
05 • REQUIREMENTS & TRACEABILITY
One limiter requirement traces to one executed result
AVIATION CONTROLS ENGINEERING ONBOARDING
30
1 • SYSTEM
PSYS-001
command-path protection
2 • SOFTWARE HLR
SWHLR-001 / PRL-001
inclusive ±12 deg/s allocation
3 • SOFTWARE LLR
SWLLR-001
apply the magnitude clamp
4 • MODEL ELEMENT
PitchRateLimiter/Pitch Rate Limiter Logic/Magnitude Clamp
5 • HARNESS
PitchRateLimiter_Harness/Unit Under Test - PitchRateLimiter
6 • EXECUTED CASE
run_pitch_rate_limiter_tests.m
“Boundary above upper limit”
7 • ITERATION 8
input 12.1 • expected 12 • actual 12
error 0 • tolerance 1e-9 • PASS
8 • ASSOCIATION
PRL-001, PRL-003, PRL-004
trace backward to intent
→
→
→
↓
←
←
←
VISIBLE RESULT • t = 0.14 s • normal_mode = true • input_valid = true • limiter_active expected/actual = true • every recorded check passed
Desktop Simulink model execution (MIL); not SIL, PIL, or HIL.
Traceability is demonstrated through CSV, script, model-path, and result associations—not live Simulink Requirements links.
Notes: Timing: 4 minutes
Read the chain in both directions: PSYS-001 to SWHLR-001 / PRL-001 to SWLLR-001 to PitchRateLimiter/Pitch Rate Limiter Logic/Magnitude Clamp to PitchRateLimiter_Harness/Unit Under Test - PitchRateLimiter to run_pitch_rate_limiter_tests.m, case Boundary above upper limit, to retained Iteration 8. The row records input 12.1 deg/s, expected 12, actual 12, zero numeric error, tolerance 1e-9, and PASS.
Caveats
- Desktop Simulink model execution (MIL); not SIL, PIL, or HIL.
- The literal AssociatedRequirement value is: PRL-001 magnitude limiting; PRL-003 status; PRL-004 50 Hz execution.
- The PSYS/SWHLR/SWLLR identifiers are illustrative mappings layered over the retained PRL association.
[Sources]
- docs/PitchRateLimiter_Requirements_Traceability.csv
- scripts/run_pitch_rate_limiter_tests.m
- results/PitchRateLimiter_TestResults.csv
- results/PitchRateLimiter_TestResults.mat

## Slide 36
05 • REQUIREMENTS & TRACEABILITY
The harness sits inside a controlled relative-file flow
AVIATION CONTROLS ENGINEERING ONBOARDING
31
data/FCS_Data.sldd
controlled parameters, buses, units, ranges
models/PitchRateLimiter_Harness.slx
stimulus + capture around the UUT
scripts/run_pitch_rate_limiter_tests.m
test driver + visible pass/fail oracle
results/PitchRateLimiter_TestResults.csv + .mat
retained machine-readable results
reports/PitchRateLimiter_TestReport.html + .png
human-readable evidence report
└ references models/PitchRateLimiter.slx
component implementation under test
↔ docs/PitchRateLimiter_Requirements_Traceability.csv
requirement-to-model/test association
HARNESS ≠ COMPONENT ≠ DRIVER ≠ REQUIREMENTS ≠ RESULTS ≠ REPORT
The two retained .mldatx files are SDI view/session artifacts. No Simulink Test or Test Manager test-suite .mldatx file is claimed.
Desktop Simulink model execution (MIL); not SIL, PIL, or HIL.
Notes: Timing: 3 minutes
Follow the companion-file flow: FCS_Data.sldd supplies controlled parameters and types; PitchRateLimiter_Harness references PitchRateLimiter; run_pitch_rate_limiter_tests drives and assesses it; the traceability CSV associates requirements; CSV and MAT retain machine-readable results; and HTML and PNG provide a reviewable report.
Caveats
- Do not claim a Simulink Test .mldatx test file exists.
- The two repository .mldatx files belong only to Simulation Data Inspector.
[Sources]
- data/FCS_Data.sldd
- models/PitchRateLimiter_Harness.slx
- models/PitchRateLimiter.slx
- scripts/run_pitch_rate_limiter_tests.m
- docs/PitchRateLimiter_Requirements_Traceability.csv
- results/PitchRateLimiter_TestResults.csv
- results/PitchRateLimiter_TestResults.mat
- reports/PitchRateLimiter_TestReport.html
- reports/PitchRateLimiter_TestReport.png

## Slide 37
06 • VERIFICATION WORKFLOW
Strong tests target boundaries, modes, failures, and timing
AVIATION CONTROLS ENGINEERING ONBOARDING
32
TEST CLASS
PITCH-RATE-LIMITER EXAMPLE
WHAT IT PROVES
Nominal
q_cmd = +5.0 → +5.0 deg/s
no unnecessary modification
Boundary
−12.0 and +12.0 → unchanged
inclusive limits
Just outside
−12.1 → −12.0; +12.1 → +12.0
correct clamping
Mode / invalid
Normal false or input invalid → specified fallback
guard and degraded behavior
Timing
step and transient inputs at 50 Hz
same-frame response / no overrun
Add combinations when requirements interact: mode × validity × boundary × schedule breakpoint.
Notes: Timing: 3 minutes
The 19-case matrix covers initialization, nominal values, inclusive boundaries, just-outside and large magnitudes, invalid or non-Normal fallback, transitions, limiter_active, timestamps, and 50 Hz spacing. Each case records actual and expected outputs rather than relying on a visual waveform judgment.
Caveats
- The PRL-004 traceability CSV says timing within 1e-12 s, while the executable uses max(1e-12, Sample_time × 1e-9), which is 2e-11 s at 0.02 s. The retained observed step is exactly 0.02 s and passes, but do not claim the script used a 1e-12 timing tolerance without reconciling the sources.
- The numeric output tolerance is consistently 1e-9 deg/s.
[Sources]
- scripts/run_pitch_rate_limiter_tests.m
- results/PitchRateLimiter_TestResults.csv
- docs/PitchRateLimiter_Requirements_Traceability.csv

## Slide 38
06 • VERIFICATION WORKFLOW
The limiter suite retains 19 passing assessments
AVIATION CONTROLS ENGINEERING ONBOARDING
33
19 / 19
ASSESSMENTS PASSED
0
FAILED
50 Hz
0.02 s SAMPLE TIME
Executed MATLAB assessments
using the standalone Simulink harness
SimulinkTestUsed = false
TestManagerFileCreated = false
Notes: Timing: 3 minutes
The retained CSV has 19 iterations and every Passed value is true; the MAT summary records Total 19, Passed 19, Failed 0; and the HTML report states PASS — 19 passed, 0 failed. The saved run used PitchRateLimiter_Harness at 50 Hz with a 0.02 s observed output step and 1e-9 deg/s numeric tolerance.
Caveats
- These are executable MATLAB assessments of a standalone Simulink harness, not Simulink Test or Test Manager results.
- A pass supports the configured classroom expectations; it is not certification approval.
[Sources]
- results/PitchRateLimiter_TestResults.csv
- results/PitchRateLimiter_TestResults.mat
- reports/PitchRateLimiter_TestReport.html
- reports/PitchRateLimiter_TestReport.png

## Slide 39
06 • VERIFICATION WORKFLOW
Callbacks create context; the test driver owns the oracle
AVIATION CONTROLS ENGINEERING ONBOARDING
34
SETUP
training_callback_
setup.m
paths • dictionary • initial state
PRELOAD
training_callback_
preload.m
deterministic stimulus
POSTLOAD
training_callback_
postload.m
solver • logging configuration
EXECUTE
run_pitch_rate_
limiter_tests.m
harness run + visible oracle
CLEANUP
training_callback_
cleanup.m
release only owned state
CONTEXT
Callbacks establish reproducible state.
ORACLE
Expected values and pass/fail logic stay in the test driver.
EVIDENCE
CSV, MAT, HTML, and PNG retain the controlled outcome.
Repeatability rule: prepare → execute → assess → retain → clean up. Dirty learner models are preserved so cleanup does not discard unsaved work.
Notes: Timing: 3 minutes
Keep lifecycle callbacks narrow and reviewable: setup establishes paths and controlled data, preload prepares deterministic inputs, post-load applies solver and logging configuration, and cleanup releases only owned resources. The test driver—not a callback—contains the case definitions, expected values, tolerances, and pass/fail assessments.
Caveats
- Callbacks must not manufacture a green result or silently discard a learner's dirty model.
- The delivered workflow uses external MATLAB functions rather than hidden model callback code.
[Sources]
- scripts/callback_workflow_example.m
- scripts/training_callback_setup.m
- scripts/training_callback_preload.m
- scripts/training_callback_postload.m
- scripts/training_callback_cleanup.m
- scripts/run_pitch_rate_limiter_tests.m
- https://www.mathworks.com/help/simulink/callback-functions.html

## Slide 40
06 • VERIFICATION WORKFLOW
FCS_Data.sldd controls shared parameters and interfaces
AVIATION CONTROLS ENGINEERING ONBOARDING
35
data/FCS_Data.sldd • shared by all eight delivered models • controlled fixed-step Sample_time = 0.02 s (50 Hz)
ILLUSTRATIVE CONTROLLED PARAMETERS
FlightControlBus — EXPLICIT INTERFACE CONTRACT
Sample_time
0.02 s
double
q_limit_normal
12 deg/s
double
pitch_Kp
0.60
double
pitch_Ki
0.025 1/s
double
pitch_rate_Kp
0.30 s
double
pitch_rate_Ki
0.20
double
q_rate
double • deg/s
Measured pitch rate
pitch_angle
double • deg
Measured pitch attitude
mach
double • 1
Illustrative Mach number
air_data_valid
boolean • 1
Validity flag
mode
uint8 • 1
0 OFF • 1 ARMED • 2 ENGAGED • 3 DEGRADED
Explicit units, types, dimensions, ranges, validity, and ownership make integration predictable—and reviewable.
Notes: Timing: 3 minutes
FCS_Data.sldd is the controlled source for Sample_time, limiter bounds, controller gains, filter coefficients, initial conditions, signal definitions, and FlightControlBus. The bus exposes q_rate, pitch_angle, mach, air_data_valid, and mode with documented types, dimensions, and units so referenced-model interfaces can update consistently.
Caveats
- A dictionary and bus establish controlled data and structure; they do not by themselves prove semantic correctness.
- The values are illustrative and not production aircraft data.
[Sources]
- data/FCS_Data.sldd
- results/FCS_DataDictionary_Inventory.csv
- results/FlightControlBus_Inventory.csv
- https://www.mathworks.com/help/simulink/ug/what-is-a-data-dictionary.html
- https://www.mathworks.com/help/simulink/slref/simulink.bus.html

## Slide 41
06 • VERIFICATION WORKFLOW
Reviewable models make intent obvious
AVIATION CONTROLS ENGINEERING ONBOARDING
36
01
NAME FOR MEANING
PitchRateLimiter, q_cmd_in, air_data_valid—not Subsystem3 or u1
02
LABEL THE CONTRACT
units, type, dimensions, sample time, range, validity, ownership
03
FLOW LEFT TO RIGHT
commands and data enter consistently; outputs leave consistently
04
ONE LEVEL, ONE STORY
use hierarchy when a reviewer cannot summarize the diagram quickly
05
REUSE CONTROLLED CONTENT
libraries and references—never copy/paste divergence
If the diagram needs a verbal apology, refactor the diagram.
Notes: Timing: 2 minutes
Reviewability comes from explicit intent at each level: meaningful names, compact interfaces, visible units and types, controlled sample times, separated responsibilities, and hierarchy that a reviewer can summarize before opening detail. Apply the checklist to one model and ask where each claim is defined and verified.
Caveats
- Good diagram appearance supports review but does not replace requirements, objective checks, configuration control, or independent verification.
[Sources]
- screenshots/VisualManifest.csv
- https://www.mathworks.com/help/simulink/ug/interface-design.html
- https://www.nasa.gov/reference/systems-engineering-handbook/

## Slide 42
07 • AUTOMATION & ENVIRONMENTS
CI automates evidence production—not approval
AVIATION CONTROLS ENGINEERING ONBOARDING
37
Commit
Jenkinsfile
Build / Update
Model Checks
Tests
Reports + Artifacts
GROOVY / JENKINSFILE
orchestrates stages, agents, parameters, parallel branches, retention
MATLAB + SIMULINK
initializes the repository, updates models, runs checks and the MATLAB harness driver; the two retained .mldatx files are SDI artifacts—not Test Manager suites
ROBOT FRAMEWORK
optional keyword-driven orchestration for benches, external interfaces, and system tests
A green pipeline is controlled evidence input—not certification approval.
Notes: Timing: 3 minutes
Treat CI as an orchestrator around controlled engineering commands: initialize, update models, run simulations and assessments, validate outputs, and retain reports. A green stage says the configured steps passed on that agent and baseline; reviewers still examine warnings, scope, traceability, failures, and configuration.
Caveats
- No Jenkins pipeline was executed for this package.
- A passing pipeline is evidence input, not certification approval.
[Sources]
- results/validation_summary.txt
- scripts/validate_training_project.m
- https://www.mathworks.com/help/sltest/ug/output-results-for-continuous-integration-systems.html
- https://www.faa.gov/documentLibrary/media/Order/FAA_Order_8110.49A.pdf

## Slide 43
07 • AUTOMATION & ENVIRONMENTS
Classify the first meaningful failure
AVIATION CONTROLS ENGINEERING ONBOARDING
38
PIPELINE FAILURE
Can you reproduce it
with the controlled command?
NO
Compare agent, licenses, paths,
project startup, data, versions
YES — compile/static
Interface • type • dimension • rate
reference • parameter • variant
YES — functional
Stimulus • expected result • tolerance
mode • initial state • timing
Fix root cause → add regression protection → re-run affected scope → run controlled full pipeline
Notes: Timing: 3 minutes
Investigate failures from the first reproducible difference: confirm release, license, paths, dictionary, model baseline, and command; then separate update/compile diagnostics from simulation or assessment failures. Correct the root cause, add focused regression protection, rerun the affected scope, and finally rerun the controlled full set.
Caveats
- Do not suppress warnings or loosen tolerances merely to create a green status.
- The validator accepts only the documented Model-block license fallback warning.
[Sources]
- scripts/validate_training_project.m
- results/validation_summary.txt
- results/environment_inventory.txt

## Slide 44
07 • AUTOMATION & ENVIRONMENTS
MIL, SIL, PIL, HIL, bench, and system integration are distinct
AVIATION CONTROLS ENGINEERING ONBOARDING
39
MIL
Model/control logic executes with model plant or model environment.
EXECUTED HERE
SIL
Generated software executes on the host using a software build.
NOT PERFORMED
PIL
Generated code executes on a target processor or representative processor.
NOT AUTOMATICALLY UNIT TESTING
HIL
Real controller/target hardware + real-time plant + physical I/O.
NOT PERFORMED
BENCH
Hardware subsystem with instrumentation, loads, and controlled stimuli.
CONCEPT ONLY
SYSTEM INTEGRATION
Integrated aircraft/system environment with representative interfaces.
CONCEPT ONLY
Desktop Simulink model execution (MIL); not SIL, PIL, or HIL.
Notes: Timing: 4 minutes
Keep execution environments distinct: MIL executes the model; SIL executes generated source code; PIL executes generated object code on a target processor; HIL uses actual controller or target hardware, physical I/O, and a real-time plant environment; bench and system-integration tests add their own controlled contexts. Name the actual environment in every retained result.
Caveats
- Desktop Simulink model execution (MIL); not SIL, PIL, or HIL.
- PIL is an execution environment and is not automatically synonymous with unit testing.
- Only call testing HIL when actual controller or target hardware, a real-time plant environment, and physical I/O are used. This package performed no HIL.
[Sources]
- results/environment_inventory.txt
- https://www.mathworks.com/help/sltest/sil-pil-and-hil-tests.html
- https://www.mathworks.com/discovery/hardware-in-the-loop-hil.html

## Slide 45
07 • AUTOMATION & ENVIRONMENTS
The current training package is internally consistent
AVIATION CONTROLS ENGINEERING ONBOARDING
40
8 / 8
DELIVERED MODELS
updated / compiled
Simulink diagram update succeeded for all eight model files.
19 / 19
LIMITER ASSESSMENTS
passed • 0 failed
Executable MATLAB assessments using the standalone Simulink harness.
24 / 24
REQUIRED EXPORTS
present
1 HTML report • 21 visual exports • 2 SDI .mldatx artifacts.
MODEL SET
AircraftFeedbackControlLoop • AutopilotModeLogic • ReferencedFlightControlArchitecture • SensorProcessingRef
PitchRateLimiter • PitchControllerRef • ActuatorCommandRef • PitchRateLimiter_Harness
“Updated” means validation compile/update succeeded; it does not mean eight files were edited.
Notes: Timing: 3 minutes
State the verified snapshot precisely: all eight delivered models completed Simulink update/compile; all 19 retained limiter assessments passed; and all 24 files in the validator's required exported-artifact list are present. The validation ran in MATLAB R2023b Update 8 on desktop Windows.
Caveats
- 8/8 models updated means SimulationCommand='update' succeeded; it does not mean eight files were edited.
- ReferencedFlightControlArchitecture and PitchRateLimiter_Harness passed with the accepted student-license fallback from Accelerator to Normal mode.
- 24/24 means one HTML report, 21 visual exports, and two SDI artifacts passed existence checks; it is not a count of every repository artifact.
[Sources]
- results/validation_summary.txt
- scripts/validate_training_project.m
- results/PitchRateLimiter_TestResults.csv

## Slide 46
07 • AUTOMATION & ENVIRONMENTS
Demonstrated evidence is narrower than certification evidence
AVIATION CONTROLS ENGINEERING ONBOARDING
41
THIS PACKAGE DEMONSTRATES
✓ Current saved models update / compile
✓ Standalone desktop MIL behavior
✓ Model-reference integration structure
✓ MATLAB-driven limiter harness assessments
✓ CSV + script + path + result associations
✓ One saved SDI run, view, and session
✓ Retained CSV, MAT, HTML, PNG, and visual exports
THIS PACKAGE DOES NOT CLAIM
× Production aircraft data or approved baseline
× Live Simulink Requirements links
× Simulink Test / Test Manager suite
× Production-code generation or code verification
× SIL, PIL, HIL, bench, or system-integration execution
× Certification approval
× Automatic compliance from a model or pipeline
Exactly two .mldatx files are retained, and both are Simulation Data Inspector artifacts.
Notes: Timing: 3 minutes
The package demonstrates saved models, controlled data, model update, desktop simulations, a standalone limiter harness, executable MATLAB assessments, CSV/script/result traceability, retained reports, and a recoverable SDI view and session. It teaches how evidence connects without overstating what was performed.
Caveats
- It does not claim production aircraft data, an approved certification baseline, live Simulink Requirements links, a Simulink Test test-suite .mldatx, Embedded Coder output, generated-code verification, SIL, PIL, HIL, Jenkins execution, or certification approval.
- The two retained .mldatx files are SDI artifacts only.
[Sources]
- README.md
- results/environment_inventory.txt
- results/validation_summary.txt
- https://www.faa.gov/regulations_policies/advisory_circulars/index.cfm/go/document.information/documentID/1032046

## Slide 47
07 • AUTOMATION & ENVIRONMENTS
Demonstrated evidence is narrower than certification evidence
AVIATION CONTROLS ENGINEERING ONBOARDING
41
THIS PACKAGE DEMONSTRATES
✓ Current saved models update / compile
✓ Standalone desktop MIL behavior
✓ Model-reference integration structure
✓ MATLAB-driven limiter harness assessments
✓ CSV + script + path + result associations
✓ One saved SDI run, view, and session
✓ Retained CSV, MAT, HTML, PNG, and visual exports
THIS PACKAGE DOES NOT CLAIM
× Production aircraft data or approved baseline
× Live Simulink Requirements links
× Simulink Test / Test Manager suite
× Production-code generation or code verification
× SIL, PIL, HIL, bench, or system-integration execution
× Certification approval
× Automatic compliance from a model or pipeline
Exactly two .mldatx files are retained, and both are Simulation Data Inspector artifacts.
Notes: Timing: 3 minutes
The package demonstrates saved models, controlled data, model update, desktop simulations, a standalone limiter harness, executable MATLAB assessments, CSV/script/result traceability, retained reports, and a recoverable SDI view and session. It teaches how evidence connects without overstating what was performed.
Caveats
- It does not claim production aircraft data, an approved certification baseline, live Simulink Requirements links, a Simulink Test test-suite .mldatx, Embedded Coder output, generated-code verification, SIL, PIL, HIL, Jenkins execution, or certification approval.
- The two retained .mldatx files are SDI artifacts only.
[Sources]
- README.md
- results/environment_inventory.txt
- results/validation_summary.txt
- https://www.faa.gov/regulations_policies/advisory_circulars/index.cfm/go/document.information/documentID/1032046

## Slide 48
08 • FIRST-WEEK TAKEAWAYS
Your first week should produce one repeatable chain
WHAT TO REMEMBER
Simulink — executable data flow, state, timing, and hierarchy
DO-178C / DO-331 — planned objectives, model role, verification, and evidence
Testing — requirements first; boundaries, modes, failures, and timing
Automation — repeatable checks and results under controlled configuration
HIL — real controller, physical I/O, real-time plant, quantitative criteria
FIRST WEEK
01 initialize folders + open the correct top level
02 update, run, stop, build, and test distinctly
03 toggle units, types, dimensions, names + badges
04 inspect one run and five signals in Data Inspector
05 trace PSYS-001 to the executed Iteration 8 PASS
06 make one controlled change; rerun affected evidence
VERIFIED STARTING POINT • 8/8 models updated • 19/19 assessments passed • 24/24 required exports present
AVIATION CONTROLS ENGINEERING ONBOARDING
42
Notes: Timing: 1 minute
Close with the working habit the learner should carry forward: choose the correct model role, make interfaces and assumptions visible, update before execution, retain objective results, and trace each claim through a controlled baseline. The next practical exercise is to reproduce one run, inspect one transient, and walk one requirement chain in both directions.
Caveats
- End on reproducible engineering practice, not on a claim of certification or HIL completion.
[Sources]
- README.md
- https://www.faa.gov/documentLibrary/media/Order/FAA_Order_8110.49A.pdf
- https://www.nasa.gov/reference/systems-engineering-handbook/